## Slide 1: Development of a close quarter, collision resistant drone (Name Needs Work)
Progress and Planning

## Slide 2: Contents
Contents
Project Background
Issues with the original scope
Year 1
Year 2
Year 3
Plans

## Slide 3: Project Background
My Interest
  Want a masters.
  Enjoy control theory.
CSIR Interest
  HCD.
  Moving into the drone space and mining research.

## Slide 4: Project Background
Initial Project Scope
  Develop an aerial platform that can autonomously navigate in an underground mine. To do inspection inside a box hole.
University Support
  Electronic System Lab (ESL), Stellenbosch University.
  Prof Japie Engelbrecht, Prof Johannes Treurnicht
CSIR Support
  Part time masters.
  20% of my time, which I have not taken
  Only 3/4 weeks taken this whole year.

## Slide 5: Issues with the original scope
Intrinsic Safety
  Defined constraints based on SA regulations
  Not a chance that drone will fly
GPS Constraints
  GPS critical part of navigation and control system
  Will need some more research, masters on it’s own
  Final Decision, Out of Scope for this project
Final Scope
  Focus on the disturbances introduced by the near wall effect and being in a confined environment.

## Slide 6: Year 1
Researched intrinsic safety and explosion protection
Wrote a proposal for a Chevron RFP, got nothing…
Taught myself some Drone and Aerodynamic Theory
Did research on the disturbances found in mines
Investigated different drone types and frames
Did a mathematical comparison of different drone types and wrote a paper for ROBMECH. Presented.
Made concept designs
Decision was made to buy a custom drone found online and focus on the control

## Slide 7: Fundamentals of Flight Theory
Mathematical Expressions for Thrust
Mass flow
Thrust
()
Pressure
Bernoulli’s Equation
Notes: Mass flow
Power into the system takes the form of a pressure differential

## Slide 8: Fundamentals of Flight Theory
Velocity Components of a Rotor
Notes: Different tip velocities
Max speed limitation

## Slide 9: Fundamentals of Flight Theory
Momentum Theory in Hover
Wake Boundary
Notes: Thrust created by the difference in Pressure between P2 and P1. Subscripts: 0 = Quiescient
1 = Just before rotor
2 = Just after rotor
inft = Far wake (one rotor diameter)

## Slide 10: Fundamentals of Flight Theory
Disk Loading
Uniform in multi rotors
Bigger Blades leads to a better efficiency.
Notes: It is easier to push large amounts of air slowly, than small amounts of air fast.
Of course bigger blades also leads to: Large rotational inertia, severely limited flight speed, bigger geometry, less immune to gusts.

## Slide 11: Fundamentals of Flight Theory
  Mathematical Relationships for Electrical Power
Electrical Power
Aerodynamic Power
Notes: Increasing Rotors doubles both the power into the system as well as the thrust where increasing the power only increases the thrust by about 1.5

## Slide 12: Selection Parameters
Efficiency, Payload and Flight Time
Flight time linked to efficiency
Single rotor is more efficient than a multi rotor of a similar size.
Multi rotors can handle bigger payloads more efficiently.
Geometry, Size and Mechanical Complexity
Design for light weight
Functional weight distribution.
Symmetrical weight distribution.
Inertia Tensor Reduction

## Slide 13: Selection Parameters
Drone Manoeuvrability Control
,
,
Fixed vs Variable Pitch.
More control surfaces gives greater manoeuvrability.
Notes: Rotation Matrix
As angle of attack changes drag increases, power consumption similar.

## Slide 14: Selection Parameters
Stability and Disturbance Rejection
Big Design Specification for this project.
Inherent Yaw Instability.
Multiple blades increases disturbance immunity.
Rotor loss

## Slide 15: Near Wall Effect
Near Wall Effect

## Slide 16: Standard Configurations
Traditional Helicopter
Low disk loading
High efficiency
Lengthy craft
High level of mechanical complexity
Very susceptible to disturbances
Limited payload

## Slide 17: Standard Configurations
Coaxial Rotors
Low disk loading
High efficiency
Compact craft
Weak lateral control
High drag during translations
Limited payload

## Slide 18: Standard Configurations
Multi Rotors
Very common design
High disk loading
Low efficiency
High payload
High disturbance rejection
Large Craft

## Slide 19: Standard Configurations
Tandem Rotors
Not a commonly used design
Jack of all trades

## Slide 20: Concept Designs
Concept Design 1 – Tandem Tilt Rotors
Pros
  Jack of all trades
  Increased manoeuvrability
  Compact Design
Cons
  Difficult to control
  Not much literature

## Slide 21: Concept Designs
Concept Design 2 – Unlike Size Quad
Pros
  High Stability
  Quadcopter manoeuvrability
  Compact Design
  Easy to control
  Higher Payload
  High Disturbance rejection
Cons
  Lower efficiency

## Slide 22: Concept Designs
Concept Design 3 – Overlapping Quad
Pros
  High Stability
  Quadcopter manoeuvrability
  Compact Design
  Higher Payload
  High Disturbance rejection
Cons
  Lower efficiency
  Slightly more difficult to control

## Slide 23: Year 2
Found a drone online
Investigated different flight controllers,
Investigated different deployable open source software
ArduPilot was the obvious decision
Look into the dev guides to ensure we have the level of access required, including simulation
Procurement of the drone
Battles with getting ardupliot to compile
Nope, still Battling…
Ardupilot Compiles
Learnt a lot of C++, still learning a lot (minimal experience prior), started playing around with the simulation.

## Slide 24: Drone 3: Mally Aeronautics
Drone 3
Pros
  Good configuration for handling the disturbances.
  Rotor protection shrouds
  Large Battery Life
  PixHawk
Cons
  Bad Mechanical Design
  Low grade materials
  Cons discovered on delivery

## Slide 25: ArduPilot: APM:Copter
Open Source Software
Pros
  Open Source & runs on the PixHawk flight controller
  Complete control of the code
  Thorough testing and usage
  Multiple ready to use utilities
Cons
  Spaghetti code with bad documentation
  A lot of inheritance in the code, difficult to follow and make sense

## Slide 26: Year 3
Set up the drone and learnt all the configuration tools, including a first flight mid year.
Started modifying the simulation code to represent our system
Spent a lot of time working through the ArduPilot code
Drew software diagrams for the code, and the implemented control loops
Started modifying parameters and then code, testing in simulation
After first flight, could not get the results from simulation as desired
Decision was made to make a Matlab/Simulink simulation
Been teaching myself Simulink and designing the simulation
Started testing with the gathered flight data
Bart arrives, adds great Simulink and theoretical control knowledge

## Slide 27: Plans
2017
  Finish Implementing the controller and plant in Simulink
  Tune the existing controllers
  Design Disturbance Observer Controller
2018 with Bart
  Implement Near Wall Effect Disturbance in Simulink
  Test Controller on it
  Debug and tune
  Generate data
2018 without Bart
  Generate last bits of needed data
  Write up, I want to ask for a month or 2 for writing up, even if I need to take unpaid leave for a bit of it

## Slide 28
Thank you
for making me do this
Angus Steele (ASteele@csir.co.za)